## Slide 1
Radon Transform Imaging
Aswin C. Sankaranarayanan
Jian Wang
Mohit Gupta
Notes: Good afternoon, every one.
The paper I am going to talk about is a novel imaging architecture for video compressive sensing

## Slide 2: Compressive Imaging
single pixel camera
(Duarte et al. 2007)
multi-pixel multiplexing cameras
(Mahalanobis et al. 2014, Kerviche et al. 2014,
Wang et al. 2015, Chen et al. 2015)
CASSI
(Gehm et al. 2007,
Wagadarikar et al. 2008)
High-speed imaging
(Reddy et al. 2011, Hitomi et al. 2011, Holloway et al. 2012)
light transport/scattering media
(Gu et al. 2008, Peers et al. 2008, S. 2009,
Sen and Darabi 2009)

## Slide 3
Spatial Multiplexing
Optically super-resolve a low-resolution sensor using a spatial light modulator
Table courtesy of Gehm and Brady, Applied Optics, 2015

## Slide 4
Spatial Multiplexing
Optically super-resolve a low-resolution sensor using a spatial light modulator
objective lens
relay lens
~ ~ ~
digital
micromirror device
(DMD)
photo-
detector
ADC

## Slide 5
Spatial Multiplexing
Optically super-resolve a low-resolution sensor using a spatial light modulator
objective lens
relay lens
~ ~ ~
digital
micromirror device
(DMD)
Low-resolution array
ADC
DMD
Low-resolution sensor

## Slide 6: Key Limitations
Achievable spatial resolution is limited to that of the DMD
  2-4 megapixels today
At least, half-the-light is lost due to spatial light modulator
Extended optical axis leads to vignetting and/or blur
objective lens
relay lens
~ ~ ~
digital
micromirror device
(DMD)
Low-resolution array
ADC

## Slide 7: Key Limitations
Achievable spatial resolution is limited to that of the DMD
  2-4 megapixels today
At least, half-the-light is lost due to spatial light modulator
Extended optical axis leads to vignetting and/or blur
  Benefits of CS are magnified at high-resolutions
objective lens
relay lens
~ ~ ~
digital
micromirror device
(DMD)
Low-resolution array
ADC

## Slide 8: Sparsity of natural images
10 megapixel image

## Slide 9: Sparsity of natural images
wavelet
transform
keep largest
K coefficients,
set others to zero
reconstruct
the image
K - # of non-zero coefficients
K/N – non-zero ratio
N pixels,
N coefficients

## Slide 10: Sparsity of natural images
Reconstruction
SNR [dB]
N [in pixels]
1E4
1E5
1E6
1E7
20
25
30
35
Non-zero ratio
K/N
N [in pixels]
1E4
1E5
1E6
1E7
0.01
0.1
128128
1 MP
20 MP
SNR > 25 dB
K/N = 0.01
K - # of non-zero coefficients
N - # of pixels
K/N = 0.1
128x128
1MP
10MP

## Slide 11: Key Limitations
Achievable spatial resolution is limited to that of the DMD
  2-4 megapixels today
At least half-the-light is lost
Long optical chain leads to vignetting and/or blur
  Benefits of CS are magnified at high-resolutions
We need a light-modulator free design for compressive imaging

## Slide 12: Radon Transform Imaging
Tomographic measurements
Key idea underlying many medical imaging techniques including CT, MRI, etc.
Key question:
Can we achieve tomographic measurements optically (for imaging in visible/infrared) ?

## Slide 13: Optical Setup
optical
axis
objective lens
cylindrical
lens
rotation
stage
line-sensor

## Slide 14: Optical Setup
Objective lens
Line Sensor
Line Sensor
scene plane
scene plane
z
y
z
x
Cylindrical lens
(focal length )
Objective lens
Cylindrical lens
(focal length )

## Slide 15: Optical Setup
optical
axis
objective lens
cylindrical
lens
rotation
stage
line-sensor
Key properties
(i) Focuses light in the direction along the line-sensor
(ii)Defocuses light in the direction perpendicular to the line-sensor

## Slide 16: Radon Transform Imaging
Recovering an image (or a video) is by solving a linear inverse problem
Many efficient solvers thanks to advances in CS and tomography/MRI.
image x
measurement y
x – image
y – measurements
A – measurement operator
Ψ – sparsifying prior

## Slide 17: Benefits of Radon Transform Imaging
Given a line-sensor with N pixels, we can (in theory) achieve a spatial resolution of NxN
  Hence, capable of achieving extremely high resolutions

## Slide 18: Benefits of Radon Transform Imaging
Given a line-sensor with N pixels, we can (in theory) achieve a spatial resolution of NxN
  Hence, capable of achieving extremely high resolutions
Fast implementation (via Fourier Slice Theorem)

## Slide 19: Benefits of Radon Transform Imaging
Given a line-sensor with N pixels, we can (in theory) achieve a spatial resolution of NxN
  Hence, capable of achieving extremely high resolutions
Fast implementation (via Fourier Slice Theorem)
No light loss
  Requires careful design of optical elements
No long light paths (no vignetting etc)
Limitations: Moving components

## Slide 20
256x256
17.7 dB
10x Comp.

## Slide 21
512x512
20.4 dB
10x Comp.

## Slide 22
1024x1024
22.1 dB
10x Comp.

## Slide 23
2048x2048
23.4 dB
10x Comp.

## Slide 24: Summary
A spatial light modulator free design for imaging in visible/IR
  Hence, capable of achieving extremely high resolutions
Has many desirable properties
  Co-axial components
  Little light loss with careful design of optical elements
  Fast implementation via the Fourier transform